## Slide 1: ROS Tutorial
Vishal Gaurav

## Slide 2: Content
Installing and configuring ROS environment
Navigating the ROS File system
Creating a ROS package
Building a ROS package
Understanding ROS nodes
Understanding ROS Topics
Understanding ROS Services and Parameters

## Slide 3: What is ROS?
The Robot Operating System (ROS) is a flexible framework for writing robot software. It is a collection of tools, libraries, and conventions that aim to simplify the task of creating complex and robust robot behaviour across a wide variety of robotic platforms.
Why? Because creating truly robust, general-purpose robot software is difficult. From the robot's perspective, problems that seem trivial to humans often vary wildly between instances of tasks and environments. Dealing with these variations is so hard that no single individual, laboratory, or institution can hope to do it on their own.
ROS was built from the ground up to encourage collaborative robotics software development
More Information

## Slide 4: Benefits of ROS
Distributed computation Many modern robot systems rely on software that spans many different processes and runs across several different computers. For example:
  Some robots carry multiple computers, each of which controls a subset of the robot’s sensors or actuators.
  Even within a single computer, it’s often a good idea to divide the robot’s software into small, stand-alone parts that cooperate to achieve the overall goal. This approach is sometimes called “complexity via composition.”
  When multiple robots attempt to cooperate on a shared task, they often need to communicate with one another to coordinate their efforts.
  Human users often send commands to a robot from a laptop, a desktop computer, or mobile device. We can think of this human interface as an extension of the robot’s software.
Important thing to note is the need of communication

## Slide 5: Cont…
Software reuse
  ROS’s standard packages provide stable, debugged implementations of many important robotics algorithms.
  ROS’s message passing interface is becoming a de facto standard for robot software interoperability, which means that ROS interfaces to both the latest hardware and to implementations of cutting edge algorithms are quite often available. For example, the ROS website lists hundreds of publicly-available ROS packages. This sort of uniform interface greatly reduces the need to write “glue” code to connect existing parts.

## Slide 6: Cont…
Rapid testing One of the reasons that software development for robots is often more challenging than other kinds of development is that testing can be time consuming and error-prone. Working with ROS provides two effective workarounds to this problem.
  Well-designed ROS systems separate the low-level direct control of the hardware and high-level processing and decision making into separate programs. Because of this separation, we can temporarily replace those low-level programs (and their corresponding hardware) with a simulator, to test the behaviour of the high-level part of the system.
  ROS also provides a simple way to record and play back sensor data and other kinds of messages. This facility means that we can obtain more leverage from the time we do spend operating a physical robot. By recording the robot’s sensor data, we can replay it many times to test different ways of processing that same data. In ROS parlance, these recordings are called “bags” and a tool called rosbag is used to record and replay them.

## Slide 7: ROS is not….
ROS is not a programming language. In fact, ROS routines are written in C++. Client libraries are available for Python, Java, Lisp, etc.
ROS is not (only) a library. Although ROS does include client libraries, it also includes (among other things), a central server, a set of command-line tools, a set of graphical tools, and a build system.
ROS is not an integrated development environment. Although ROS does not prescribe any particular development environment, it can be used with most popular IDEs.

## Slide 8
For a detailed information about ROS including both tutorials and reference materials please see
  ROS Wiki
  Reference
  Tutorials
  Help forum

## Slide 9: Core components

## Slide 10: Installing and configuring ROS Environment
For details about installation please visit
http://wiki.ros.org/ROS/Installation
For Baxter
For TurtleBot